Plastics 001	                                             	    Name__Master_______________

______________

Quiz #8                               		           22                                        Date____________________

- In Injection Molding, the polymer is melted to make it flow into the mold.  What is done to the polymer sheet/film to make it take the shape of the mold in Thermoforming? (2 pts)

____Soften___________________________________________________________________________________________

- What type of sheet is used to make short run and thicker Thermoforming parts?(2 pts)

___Flat______________________________________________________________________________

- What is the maximum pressure used in Vacuum Forming? (2 pts)

____14.5/14.7 psi__________________________________ ___________________________________________________

- Which Thermoforming process is the most common? (2 pts)

___Vacuum Forming___________________________________________________________________________________

- If you were looking to build a Thermoforming mold for a decorative bathroom sink and there was plenty of money to build a mold, what mold type would you use? (2 pts)

___Male_____________________________________________________________________________________________

- What are the three hollow parts processes? (2 pts)

___Blow Molding, Rotational Molding, and Twin/Dual Sheet Thermoforming______________________________________

- What causes the build-up of polymer after the first layer of powder has melted onto the mold wall in Rotational Molding?  (2 pts)

___The polymer that is melted on the mold wall becomes tacky and picks up more powder as it rotates under the powder pool_________________________________________________________________________________________________

- Name 2 advantages of Rotational Molding: (2 pt each)

  - _Low Tooling Cost, Complex Shapes, Low Stresses, Uniform Wall Thickness_

  - _Good Surface Detail, Double Wall, and Thickness Manipulation__________

- Name 2 disadvantages of Rotational Molding: (2 pt each)

  - _Long Cycles, Limited Materials, Warpage,____________________________

  - _and Secondary Operations ________________________________________